## Slide 1: Hamming Code
By Andres Blandon

## Slide 2: Hamming Code
Hamming code is a set of error-correction code s that can be used to detect and correct bit errors that can occur when computer data is moved or stored.
Named after R.W. Hamming of Bell Labs

## Slide 3: Calculating Hamming Code
For this example we will use this byte of data: 10011010
Create the data word, leaving spaces for the parity bits: _ _ 1 _ 0 0 1 _ 1 0 1 0 Calculate the parity for each parity bit (a ? represents the bit position being set):
Position 1 checks bits 1,3,5,7,9,11: ? _ 1 _ 0 0 1 _ 1 0 1 0. Even parity so set position 1 to a 0: 0 _ 1 _ 0 0 1 _ 1 0 1 0

## Slide 4: Calculating Hamming Code (cont.)
Position 4 checks bits 4,5,6,7,12: 0 1 1 ? 0 0 1 _ 1 0 1 0. Odd parity so set position 4 to a 1: 0 1 1 1 0 0 1 _ 1 0 1 0
Position 8 checks bits 8,9,10,11,12: 0 1 1 1 0 0 1 ? 1 0 1 0. Even parity so set position 8 to a 0: 0 1 1 1 0 0 1 0 1 0 1 0
Code word: 011100101010.