## Slide 1: TCP Congestion Controls: Tahoe, Reno, Vegas
By Andres Blandon

## Slide 2: What is Congestion Control?
TCP (Transmission Control Protocol) uses network congestive-avoidance algorithms in order to control congestion when data is being transported
Congestion-avoidance algorithms are the primary basis when trying to manage congestion during the flow of data
These controls are a function of internet host rather than networks themselves

## Slide 3: TCP Tahoe
In TCP Tahoe, when data loss occurs, a fast retransmit
Half the current congestion window is saved as slow start threshold (SSThresh), and slow start begins again from its initial congestion window
Once the congestion window reaches the SSThresh, TCP will change its congestion avoidance-algorithm where each new acknowledgement increases the congestion window by maximum segment size/ congestion window
This results in a linear increase of the congestion window
Congestion window is reduced 1 maximum segment size

## Slide 4: TCP Reno
TCP Reno is essentially the same thing as TCP Tahoe
The difference between them is the addition of the fast recovery implementation in TCP Reno
The sequence begins with a fast retransmit after a loss of data occurs, the congestion window is then cut in half and saved as SSThresh for a new congestion window
But, TCP Reno skips the slow start process and goes directly to the congestion-avoidance algorithm
Congestion window is still reduced 1 maximum segment size

## Slide 5: TCP Vegas
The unique function of TCP Vegas in which timeouts were set and round-trip delays were measured for every packet in the transmit buffer
Also, TCP Vegas uses additive increases in the congestion window
Vegas emphasizes packet delay rather than packet loss
The algorithm depends heavily on the accurate calculation of the base ping time
TCP Vegas is renowned for its smooth and fluid functionality