## Slide 1: IP/TCP
By Andres Blandon

## Slide 2: What is IP/TCP?
IP – Internet Protocol
TCP – Transmission Control Protocol
TCP/IP involves the transport layer in networking.
Transport layer protocols supply a header field to identify a the Application Layer
Provide reliability and flow control for applications that transfer large amounts of data

## Slide 3: Role of TCP
There are two protocols that work in this layer: TCP and UDP
  Transmission Control Protocol (TCP) is connection oriented and designed for reliable transfer of information in complex internetworks
  User Datagram Protocol (UDP) is connectionless and designed for efficient communication of small amounts of data.
Work with segments (TCP) or datagrams (UDP)
Provide a way to identify the source and destination applications involved in a communication
Protect data with a checksum

## Slide 4: Segments and Datagrams
TCP works with units of data called segments
UDP works with units of data called datagrams
Based on the required services of the Application Layer, data is sent to either TCP or UDP, which adds a header to the data
The Transport Layer Protocol then passes the segment or datagram to the Internet Layer Protocol, usually IP
The Internet layer deencapsulates the packet with the data and sends it back to the Transport Layer
The Transport Layer processes, deencapsulates, and sends the resulting data back to the Application Layer

## Slide 5: Identifying Source and Destination Applications
The Transport-layer header provides the information needed to determine the application the received data is sent to
TCP and UDP use a port number to specify the source and destination Application-layer protocols
the MAC address and IP address get the packet to the computer, and the port number gets the data to the application

## Slide 6: Protecting Data with Checksum
To protect data integrity, TCP and UDP provide a checksum, similar to CRC (Cyclic Redundancy Check)
Routers and switches have been known to corrupt data, recalculate the CRC code, and send the corrupted data
Intermediate devices don’t recalculate the checksum in the Transport layer, so if data corruption occurs along the way, the final receiving station detects the checksum error and discards the data

## Slide 7: TCP Handshake
A TCP session begins when a client sends a TCP synchronization (SYN) segment to the destination device, usually a server
A destination port number is specified, and a source port number is assigned
When the server receives the SYN segment, it usually responds by sending one of two segments: an acknowledgement-synchronization (ACK-SYN) segment or a reset connection (RST) segment
If an RST segment is returned, the server refused the request to open a session. If an ACK-SYN segment is returned, the client completes the three-way handshake by sending an ACK segment back to the server

## Slide 8: Flow Control with Acknowledgements
TCP provides flow control, which prevents a destination from becoming overwhelmed by data, resulting in dropped packets
TCP does this by establishing a maximum number of bytes, called the window size, that can be sent before the destination must acknowledge receipt of the data
If a sending machine hasn’t received an acknowledgement before sending the number of bytes established by the window size, it stops sending data
If no acknowledgement is received in a specified timeout period, the sender retransmits the data from the last acknowledgement received

## Slide 9: Defines and Verifies IP Addresses
An IP address is assigned to every computer and network device using TCP/IP for communication
IP addresses are used for two main purposes:
  to identify a network device at the Inter- network layer and
  to identify the network on which a device resides
When an IP address is assigned to a computer or network device, the host’s Internetwork-layer identity is defined
When a host receives an IP packet, it compares the packet’s destination IP address with its own address to verify that the packet was delivered correctly
If the destination address matches or is a broadcast or recognized multicast address, the packet is processed; otherwise, it’s discarded

## Slide 10: Routes Packets through internetwork
Routers work at the Internetwork layer, and their job is to select the best path to the destination
If a path becomes unavailable or congested, they select an alternative, if available
Routers use the network ID portion of IP addresses along with their routing tables to determine on which network a destination device can be found and the best way to get packets to their destination

## Slide 11: Resolves MAC Addresses from IP Addresses
When a packet is ready to be sent to the Network access layer, the destination device’s MAC address must be retrieved before the frame header can be constructed
TCP/IP uses Address Resolution Protocol (ARP) to accomplish this
ARP returns a computer’s MAC address by querying the network to determine which computer is assigned a particular IP address

## Slide 12: Delivers Packets Efficiently
Internetwork protocols rely on protocols in the Transport and Application layers to provide advanced reliability features
Protocols at this layer are concerned with one packet at a time, with no concern for packets that came before or after it and with no confirmation that delivery was successful
This communication strategy is called connectionless communication and protocols using it are called connectionless protocols
When using a connectionless protocol, no lasting connection is made from source to destination. A connectionless protocol relies on an upper-layer protocol to ensure the packet’s travel is safe